Data Representation II

Number Base Addition

Addition  in different number bases operate in the same  ways  as for decimal but remember that the highest value possible in  each position is one less than the base value.

Addition

Decimal	Binary 		     Octal     	        Hex

5 		101		5        		5

6 +          	110 +     	6  +     		6  +

11         	         1011                 13        		B

1           	              1          	              1

Decimal      	Binary    	    Octal     	       Hex

25	        11001      	31       		19

21 +	        10101 +     	25 +    		15 +

46              101110      	56       		2E

1      1

Subtraction

All mathematical operations take place as a form of addition!

The computer does not actually do subtraction!

Subtraction  is  achieved  by 'complementing' the  number  to  be subtracted and then adding the numbers.

What is complementing?

"The complement of a number is the value which when added to

the  original  number  gives a value equal  to  the  highest

available digit of the number base."

Is that clear?

In the decimal system the complement of 2 is 7 because 2+7  gives 9.  Nine  is  the  highest available digit, so  7  is  the  nines complement of 2, and vice versa.

In  the binary system the complement of 1 is 0 because 1+0  gives 1.  One  is  the  highest  available digit,  so  0  is  the  ones complement of 1, and vice versa.

So the ones complement of 	1110101

is                              		0001010

Within  the computer, however, TWO's complement is used. To  find the twos complement simply add 1 to the one's complement.

Value               		1110101

ones complement	0001010

add 1                     		1 +

twos complement     	0001011

Subtraction example

In decimal 5-2 = 3

In  binary the numbers must be expressed as equal length  numbers (add  leading zeros if needed) and so must the answer. Any  final carry is ignored.

5=     101                          			101

3=     011   ones complement  	100

1 +

twos complement  	101    new sum 101 +

010                                                 						          1                carry ignored

final answer = 010    = decimal 2

Exercise 2.1

prove that	a) 10 -2 = 8    d) 32 -26 = 6

b) 12 -7 = 5    e) 45 -25 = 20

c) 16 -8 = 8    f) 59 -33 = 26

Fixed Length Computer Words

Data  of  any sort is represented in the computer in BITS,  as  a series of zeros and ones.

A BIT is either 0 or 1.

Eight BITS equal one BYTE.

A  WORD equals the number of BITS which the computer treats as  a single  unit,  i.e. "the word length is 16 bits."  or  "the  word  length is 32 bits.", etc. We shall use an 8 bit word for the time being.

Within  the  CPU  data is held in registers. An  8  bit  register holds, not surprisingly, 8 bits.

The  ascii  code  for A is 65. If this were stored in  an  8  bit register:

01000001

The  decimal  value 7 is binary 111. If this were stored  in  the computer in an 8 bit word leading zeros would be added to become:

00000111

To perform the decimal sum 14 + 5 using an 8 bit register:

14     Becomes	00001110

5     Becomes	00000101 +

00010011   = 19

Representation of Negative Numbers

In  the decimal system a negative number has a minus (-) sign  in  front of it, i.e. -7. But the registers can only store 0 or 1.

Methods used to represent signed numbers:

a) Signed magnitude

In  the decimal system a sign may be placed in front of  the

number to indicate positive or negative.

85 or +85 is positive

-85 is negative

There is a sign and the magnitude of the number.

In each register the most significant bit (MSB) is the left  most

digit.  This  is used to represent the sign of  the  number.    0

means it is positive, and 1 means it is negative. The rest of the

bits are used to represent the value.

The weighting of the digit positions becomes:

To represent -85 in an 8 bit register:

+85 =     01010101           MSB is 0 = positive

-85 =      11010101           MSB is 1 = negative

neg   64    +   16   +   4   +   1  = -85

b) Radix (or base) complement

We have used this already in the example of subtraction.

The weighting of the digit positions changes:

This is best shown as an example:

To represent -85 in an 8 bit register:

+85 =     01010101           MSB is 0

10101010          The ones complement

1 +       Add one for the

10101011          twos complement

-128          +   32           +   8              +   2      + 1 = -85

Exercise 2.2

Represent  the  following  numbers in  sign  magnitude  and  twos complement in an 8 bit register:

a) 32		b) -1		c) 52

d) -99             e) 110               f) -64

Range Limitation Numbers

The  range  of values that can be represented is limited  by  the size  of  the register used. There is the  possibility  that  the result of an operation will produce a result that is too large or small to be represented in the available registers. The technical term for this is 'overflow'.  Multiple register could be used but this involves using more memory and more complex processing.

For an 8 bit register:

Sign magnitude:

Max positive   01111111   = 127

Min negative   11111111   = -127

For twos complement:

Max positive   01111111   = 127

Min negative   10000000   = -128

You  can  calculate  the  range of a  register  when  using  twos complement with the following formula:

Max  =     2(n-1) -1

Min  =    -2(n-1)

Where n is the number of bits in the register

i) for an 8 bit register

Max      27-1 = 127

Min     -27   = -128

ii) for a 16 bit register

max	....................

min	....................

iii) For a 32 bit register

max	.....................

min .......................

A  16 bit word (register) is standard for integer.  However,  for greater precision (double precision) two words may be used.

Range for single precision (16 bit word) = -32,768    to    32,767

Range for double precision (2 words)     = -2,147,483,647     to    2,147,483,646