Central Processing Unit

REGISTERS

MAR	Memory Address Register

MBR	Memory Buffer Register

CIR 	Current Instruction Register.	Temp. storage location for 'words' read from memory.

Could be data or program instruction.

Instruction Register     -program instructions

Data Register		-data

PROGRAM 	= Sequence of instructions

FETCH EXECUTE CYCLE =

This cycle of events is called the Fetch Execute Cycle

The Central Processing Unit

PC		Program counter

Location in memory of next instruction

-incremented after each Fetch.

CIR	Current Instruction Register

Intruction read from memory.

MBR	Memory Buffer Register

Temp. storage for data between memory and Accumulator.

MAR	Memory Address Register

Address of data in memory to be

Fetched to MBR

Accumulator

General registers in the ALU.	Working area for data (add, sub, etc.)

Memory Model of a Program

Program has 4 segments:

The Fetch Execute Cycle

Fetch

PC copied to MAR  -location of next instruction

Memory to MBR       -contents of location is	read to MBR

Increment PC		-Point to location of following instruction

MBR copied to CIR   -ready to be decoded.

Execute

CIR instruction decoded   by the Control Unit

Instruction executed	      by the Control Unit

Cycle repeated   (until instruction is STOP)

FEC Flowchart

Exercise 1

Draw a labelled diagram of the CPU & indicate each step of the Fetch Execute Cycle.

MACHINE INSTRUCTIONS

INSTRUCTION SET  = All available instructions

TYPE OF INSTRUCTION

=Arithmetic and logical operations

=Input and output operations

=Branching -sequence of instructions

=Moving data   -inside CPU   or   between CPU & Memory

INSTRUCTION FORMAT

OPCODE	operation to be performed ADD, MOVE, etc.

OPERAND          Memory address of data to be used.

-Three Address Instruction

Operation involves three objects:

ADD  a,b,c	;add b & c store result in a

-Two Address Instruction

Operation involves two objects:

ADD a,b		;add a to b

-One Address Instruction

Operation involves one object (assume use of Accumulator):

Three instructions to increment a number...

lda   X		;place x into Accumulator

add   Y		;add Y to value in Accumulator

sto   Z		;Store value in Accumulator at Z

-No Address Instruction

Uses the Stack.

Push		;contents of accumulator placed on stack.

Pop		;item at top of stack placed in accumulator (& removed from stack)

Exercise 2

1)	What is the highest memory location that can be addressed in each of the instruction formats?

3 address = 4 bits = 15

2 address = 6 bits = 63

1 address = 12 bits = 4095

Typical Instruction Set

Actual instructions depend on individual computer.

Operation			80x86 processor

Add				ADD		Addition

Subtract			SUB		Subtraction

Multiply			MUL		Multiplication

Divide				DIV		Division

Branch				Jn		Jump (various)

Register			MOV	           Move data between registers

Stack				PUSH	     	Place on stack

POP	     	Remove from stack

Input				IN		Input from port

Output				OUT		Output to port

Logical:

And				AND

Or				OR

Not				NOT

Example Assembler Program

; Program to add two numbers 16 & 32

;

mov	ax,10h		;move 10hex to acc.

add	ax,20h		;add 20hex to value in acc.

int	21h		;interrupt 21 output acc to screen.

Exercise 3

Complete the Assembler tutorial & exercises

INPUT/OUTPUT

Instructions to transfer data between peripherals and main memory.

Direct Memory Address DMA

Data transfer controlled by peripheral (CPU continues normal processing)

Data transfered in block.

Example : Read data from disk to memory

PROGRAMMED INPUT/OUTPUT

Four Input/output instructions:

a)   Input -transfer data from peripheral to CPU.

b)   Output -transfer data from CPU to Peripheral.

c)   Set Control Flags

d)   Test Control Flags

Flag (busy)	Set by CPU when data transfer in process.

Flag (done)	Set by peripheral when data transfer complete.

Data Buffer	Stores data during transfer.

Program control via:

a)   Interrupt	-from peripheral to tell CPU transfer complete.

b)   Polling	-Set busy flag & test done flag until transfer complete.

(inefficient -waste time continually checking)

Memory Addressing Modes

The physical memory addresses used by the hardware are the actual address in memory. Addressing memory locations directly restricts the size of usable memory. Therefore a method of addressing locations beyond this limit are required. The addressing mode used is indicated in the operand of an instruction.

The following addressing modes are common to most computers:

Register Addressing

Data moved between registers in the CPU.

ie

MOV	AX,BX

MOV	DX,CX

MOV	DI,SI

Immediate Addressing

Moving a constant numeric value to a register, or to a memory location.

ie

MOV	AX,5

MOV	BL,RED	; where RED has been defined as a numeric value

MOV  ADD1,RED  ;where ADD1 has been defined as a memory address

Direct Addressing

Moving data from a memory location to a register, or vice versa.

ie

MOV  AL,ADD1	;where ADD1 has been defined as a memory address

MOV  ADD2,AH

Indirect Addressing

Using the registers to point to a memory location which itself holds a pointer to the data to be used.

ie

MOV  ADD1,5	;ADD1 stores the value 5

MOV	SI,ADD1	;register SI stores the address of ADD1

MOV	AX,[SI]	;AX stores the value from the address in SI

# Text boxes

The Fetch Execute Cycle

ES

SS

DS

CS

Extra

Stack

Data

Code

Temporary Storage

Stores Instruction location when program branches.

Variables

Instruction Sequence