1) Draw the circuit and truth tables for the following:

_____            _                  _    _

a)  A + B       b)  X . Y       c) A + B       d) A + B + C      e) A . B + C

AND has precedence over OR.

2) Three  inputs  are  used to store a numeric value  (0  to  7).  A circuit is required to detect a value greater than 4, that is the values 5, 6 and 7, by producing an output of one.

value	A	B   	C     	OUTPUT

0      	0   	0   	0       	0

1      	0   	0   	1       	0

2      	0   	1   	0       	0

3      	0   	1   	1       	0

4      	1   	0   	0       	0

5      	1   	0   	1       	1

6      	1   	1   	0       	1

7      	1   	1   	1       	1

_                _

A.B.C + A.B.C + A.B.C

Draw the Circuit and its Truth Table for this expression:

3)  Four binary signals A, B, C, D represent single Binary Coded Decimal (BCD) digit.  A logical circuit is required to output logic 1 on the occurance of an invalid combination of the signals, that is, when they represent a number in the range 10 to 15.

i)  	The inputs to the circuit are clearly defined and it is assumed that A is the most significant digit and D is the least significant digit.

ii)  	The single output is to be 1 when the binary number represented by the input ABCD is in the range 10 to 15 (binary 1010 to 1111)

iii)  	The truth table has 16 entries -representing the numbers 0 to 15

INPUTS

A     B     C     D	     OUTPUT

0	0      0      0      0		0

1	0      0      0      1		0

2	0      0      1      0		0

3	0      0      1      1		0

4	0      1      0      0		0

5	0      1      0      1		0

6	0      1      1      0		0

7	0      1      1      1		0

8	1      0      0      0		0

9	1      0      0      1		0              _     _

10	1      0      1      0		1	A B C D        _

11	1      0      1      1		1                 _  _      A B C D

12	1      1      0      0		1	A B C D             _

13	1      1      0      1		1                     _      A B C D

14	1      1      1      0		1          A B C D

15	1      1      1      1		1                             A B C D

Draw the circuit

4) Give and example of the use of the following gates   NAND,  NOR,  XOR include a circuit and Truth Table.

# Text boxes

# Boolean Review Test