| Embedded System | An embedded system is some combination of computer hardware and software, either fixed in capability or programmable, that is specifically designed for a particular kind of application device. Industrial machines, automobiles, medical equipment, cameras, household appliances, airplanes, vending machines, and toys (as well as the more obvious cellular phone and PDA) are among the numerous possible hosts of an embedded system. Embedded systems that are programmable are provided with a programming interface, and embedded systems programming is a specialized occupation. |
| --- | --- |
| Domestic Appliance | Machines found around the house such as: Washing Machine, microwave, television, etc. |
| High Level Programming | A computer programming language using command statements, symbols and words that resemble English-language statements. FORTRAN, Pacal, C, PL/1, COBOL, and BASIC are high level languages. Each command/ instruction is the equivalent of many machine language instructions. |
| Low Level Programming | Any programming language which either is assembly language, or which is meant to be closely related to, and easily translated into, machine language. Low-level languages lack the amenities of high-level languages but it may be possible to write more efficient code in them |
| Loop Control | Many real-time embedded systems make control decisions. These decisions are usually made by software and based on feedback from the hardware under its control (termed the plant). Such feedback commonly takes the form of an analog sensor that can be read via an A/D converter. A sample from the sensor may represent position, voltage, temperature, or any other appropriate parameter. Each sample provides the software with additional information upon which to base its control decisions |
| Closed loop & Open loop | Systems that utilize feedback are called closed-loop control systems. The feedback is used to make decisions about changes to the control signal that drives the plant or hardware. An open-loop control system doesn't have or doesn't use feedback. |
| Binary |  |
| Hexadecimal (hex) | Also called Hex codes. Numbers and letters (0,1,2,3,4,5,6,A,B,C,D,E,F) derived from base-16 mathematics. Often used as a shorthand version of binary numbers: i.e. 10010100101011101101 binary = 94AED hex |
| Binary Coded Decimal (BCD) |  |
| Logical Operators | Operators, such as AND, OR, NOT that take two boolean operands and produce a boolean result (True or False). Used as part of a boolean expression, often in the condition of a control structure such as and IF or WHILE statement. And TRUE only when all inputs are true Or TRUE if any input is true Not reverses the input i.e. True becomes False / False becomes True. |
| Fixed Point Number |  |
| Floating Point Number | System in which the location of the decimal point is indicated by an exponent of the radix. The number is recorded in two parts: mantissa and exponent. The mantissa stores the digits and the exponent records where to place the decimal point. Mantissa Exponent Actual value Denary 2345 2 23.45 2345 -2 0.002345 Binary 100101 11 ( which is 3) 100.101 100101 -11 (which is –3) .000100101 |
| Microcontroller |  |
| Port |  |
| ADC |  |
| DAC |  |
| Sensor | A device that responds to a physical stimulus (heat, light, sound, pressure, motion, flow, and so on), and produces a measurable corresponding electrical signal |
| Signal Conditioning | The process of making a sensor signal compatible with the data acquisition hardware. Signal conditioning includes amplification, filtering, electrical isolation, and multiplexing. Generically describes circuitry used to manipulate or modify analog or digital signals. Makes a signal suitable for input to an analog-to-digital converter. For example, a signal may be filtered to remove noise, or amplified to meet the range of the A/D converter. |
| Noise Filtering | Removing noise from an input or output channel leaving clearer signal. |
| Linear | Having an output that varies in direct proportion to the input. If the input is increased by a factor of, say 1.2, then the output increases by a factor of 1.2, no more and no less. This is the ideal for all parts of a sound system, since no distortion is introduced. |
| LCD -Liquid Crystal Display |  |
| Relay | A Solid State relay is a switching device that completes or interrupts a circuit electrically and has no moving parts. A Mechanical relay is an electromechanical device that closes contacts to complete a circuit or opens contacts to interrupt a circuit. |
| Motor |  |
| Solenoid | An electrical conductor wound into a cylindrical coil; when electric current flows through the coil, the magnetic field about the solenoid is similar to that about a bar magnet. Solenoids are electromagnetic switches. The magnetic field moves a metal piston, which is connected to a mechanism that performs a function. The function may be the moving of a valve, switch, or mechanical linkage. |
| Sampling |  |
| Digital Filter | A filter which acts on data after it has been sampled and digitized. A filter that slows the response of a system when inputs change unrealistically or too fast. The parameters of digital filters are generally more stable than the parameters of commonly used analog (continuous) filters. |
| Feedback | the process in which part of the output of a system is returned to its input in order to regulate its further output. The return of a portion of the output of a device to the input; positive feedback adds to the input, negative feedback subtracts for the input. |
| PID |  |
| PWM | A switch-mode control method used in amplifiers and drivers to control motor voltage and current to obtain higher efficiency than linear control. PWM refers to variable on/off times (or width) of the voltage pulses applied to the transistors. |
| DC |  |
| I/O | Stands for "Input/Output," in automation, a term encompassing all physical connection points between a control system and the sensors and actuators of the "real world." |
| PLC |  |
| bit |  |
| PROM & EPROM |  |

# Text boxes

### Control Technology – Glossary of Terms

by